## Slide 1
Qwen3-VL-32B-FP8 Same-Host Aggregate vs Disagg Status Report
Performance Analysis Across 4 Workload Cases & Bottleneck Identification — 2026-05-31
Key Findings
• TP=1 Aggregate beats Disagg E/PD in every workload tested (np=128 × {rate=1.0, 2.0})
• Aggregate: 100% success (128/128 in all 8 benches); Disagg: 4 of 8 benches had 16-49% failures
• Speedup: Aggregate 2.0–2.7× faster RPS in heavy workloads; 1.0–1.3× in light
• Latency: Aggregate up to 16× lower at low concurrency (8img/768p median E2E 5.3s vs 84.9s)
• Disagg same-host has no measured benefit vs aggregate in any case
Test Matrix
Setup | Encoder | Decoder | Transport
Aggregate TP=1 | Same process, GPU 1 | Same process, GPU 1 | None (in-memory tensor)
Disagg E/PD | GPU 0 (separate process) | GPU 1 (separate process) | NIXL-write over NVLink (cuda_ipc)
Workloads & Parameters
• 4 Workloads: 8img/1080p, 16img/768p, 8img/768p, 4img/768p
• 2 Rates: 1.0 and 2.0 RPS | np=128 prompts | output_len=256 tokens | seed=0
• Hardware: H200 GPU, mem-fraction=0.85, max-running-requests=64, chunked-prefill-size=16384
• Disagg encoder/decoder split across GPU 0 / GPU 1 (NVLink, NIXL_WRITE mode)

## Slide 2
Slide 2 — Headline RPS Comparison
RPS at np=128 for 8 aggregate + 8 disagg benches (16 total). Speedup column shows Agg/Disagg ratio.
Workload | rate | Agg RPS | Disagg RPS | Agg/Disagg | Agg Success | Disagg Success
8img/1080p | 1.0 | 0.47 | 0.23 | 2.0× | 128/128 ✓ | 65/128 ✗
8img/1080p | 2.0 | 0.49 | 0.18 | 2.7× | 128/128 ✓ | 51/128 ✗
16img/768p | 1.0 | 0.71 | 0.34 | 2.1× | 128/128 ✓ | 77/128 ✗
16img/768p | 2.0 | 0.76 | 0.33 | 2.3× | 128/128 ✓ | 72/128 ✗
8img/768p | 1.0 | 0.90 | 0.70 | 1.3× | 128/128 ✓ | 128/128 ✓
8img/768p | 2.0 | 1.49 | 0.67 | 2.2× | 128/128 ✓ | 107/128 ✗
4img/768p | 1.0 | 0.99 | 0.98 | 1.0× | 128/128 ✓ | 128/128 ✓
4img/768p | 2.0 | 1.93 | 1.79 | 1.08× | 128/128 ✓ | 128/128 ✓
Patterns
• Agg never fails; Disagg fails on 4 of 8 benches with 16-49% loss rate
• Agg RPS rises with rate (6 of 8 cases improve from r=1.0 → r=2.0)
• Disagg RPS stagnates or drops with rate (5 of 8 cases worsen or flat)
• Largest speedup at 8img/1080p r=2.0 (2.7×) and 16img/768p r=2.0 (2.3×)

## Slide 3
Slide 3 — Latency Comparison (Median E2E and TTFT)
Aggregate consistently faster; 16× advantage at 8img/768p r=1.0 due to no NIXL handoff queue.
Median End-to-End Latency (s)
Workload | rate | Agg E2E | Disagg E2E | Disagg/Agg
8img/1080p | 1.0 | 148.7 | 175.4 | 1.18×
8img/1080p | 2.0 | 187.7 | 214.9 | 1.14×
16img/768p | 1.0 | 80.5 | 163.2 | 2.03×
16img/768p | 2.0 | 109.1 | 155.7 | 1.43×
8img/768p | 1.0 | 5.3 | 84.9 | 16.0×
8img/768p | 2.0 | 33.8 | 109.9 | 3.25×
4img/768p | 1.0 | 2.9 | 6.5 | 2.24×
4img/768p | 2.0 | 2.7 | 11.7 | 4.33×
Median TTFT (s)
Workload | rate | Agg TTFT | Disagg TTFT
8img/1080p | 1.0 | 82.3 | 112.0
8img/1080p | 2.0 | 107.7 | 169.9
16img/768p | 1.0 | 36.2 | 71.4
16img/768p | 2.0 | 78.2 | 104.9
8img/768p | 1.0 | 1.7 | 39.9
8img/768p | 2.0 | 9.2 | 60.4
4img/768p | 1.0 | 0.7 | 2.5
4img/768p | 2.0 | 0.7 | 3.3
Key Insight
• Latency gap is largest at medium load (8img/768p r=1.0): Agg returns first token in 1.7s, Disagg in 39.9s
• Disagg's NIXL handoff + PD admit queue dominates time-to-first-token under any non-trivial load
• Even 4img/768p (where RPS is identical) shows Agg 2-4× lower E2E from saved handoff cost (~150ms+queue)

## Slide 4
Slide 4 — Total Token Throughput (GPU Compute Utilization)
Validates: RPS = total_tput / per_req_tokens (verified within 1.2% on all 16 datapoints)
Workload | rate | Agg tput (tok/s) | Disagg tput | Agg/Disagg
8img/1080p | 1.0 | 7,787 | 3,781 | 2.06×
8img/1080p | 2.0 | 8,033 | 2,975 | 2.70×
16img/768p | 1.0 | 8,934 | 4,242 | 2.11×
16img/768p | 2.0 | 9,553 | 4,109 | 2.32×
8img/768p | 1.0 | 5,704 | 4,470 | 1.28×
8img/768p | 2.0 | 9,481 | 4,282 | 2.21×
4img/768p | 1.0 | 3,233 | 3,198 | 1.01×
4img/768p | 2.0 | 6,306 | 5,856 | 1.08×
Throughput Trend r=1.0 → r=2.0
Workload | Agg Δ | Disagg Δ
8img/1080p | +3% | -21%
16img/768p | +7% | -3%
8img/768p | +66% | -4%
4img/768p | +95% | +83%
Conclusion
• Aggregate's GPU compute throughput climbs with rate in heavy cases (proves NIXL is the bottleneck for disagg)
• Disagg's GPU compute throughput drops with rate in heavy cases (NIXL backpressure starves the GPU)
• GPU compute is the ceiling for agg; NIXL handoff is the ceiling for disagg

## Slide 5
Slide 5 — Case 1 Bottleneck: 8img/1080p (input_len = 16,420)
Heaviest case. KV pool 74% saturated, chunked-prefill produces 40-46% small-batch tails. Disagg fails ~50%.
Workload Profile
• 8 images × 1920×1080 → 16,420 input tokens (just above chunked_prefill_size=16,384)
• KV demand per req: 16,692 tokens; theoretical KV cap: 41 in-flight
• Embedding size per request: ~134 MB
Disagg Bottlenecks (RPS=0.18-0.23, ~50% failures)
• #1 Chunked-prefill split tail: 40-46% of prefill batches are <500-token tails
• #2 KV pool 74% saturated: in-flight capped at 31
• #6 NIXL buffer exhaustion: 768 MB pool only fits 5-6 of 134 MB embeddings
Agg Behavior (RPS=0.47-0.49, 100% success)
• Same chunked-prefill split tails (40-42%) — STRUCTURAL TO SGLANG, NOT FIXED BY AGG
• But no NIXL handoff → no buffer pool to exhaust → 0 failures across 256 requests
• in-flight 67-83 (limited by max_running_requests=64 + GPU compute, agg-side)
Improvement Methods
Method | Effect | Cost
--chunked-prefill-size 32768 | Tail eliminated, RPS 0.47 → ~0.65 (estimate) | Per-batch GPU mem 2×, may OOM
TP=2 aggregate (2 GPUs) | RPS 0.47 → ~0.95 (per existing data) | 2 GPUs
Patch SGLang scheduler tail-coalescing | RPS 0.47 → ~0.55 | Multi-day SGLang patch
Use smaller image (768p) | RPS 0.47 → 0.71-0.90 | Resolution change

## Slide 6
Slide 6 — Cases 2 & 3 Bottleneck: 16img/768p (12,401) & 8img/768p (6,238)
16img: KV pool 98% saturated. 8img: max_running_requests=64 cap + batch degradation under load.
16img/768p — input_len 12,401 (76% of chunked_prefill)
• Disagg (RPS=0.33-0.34, 40% failures):
• #2 KV pool truly saturated: in_flight=54, KV usage 98% (54 × 12,673 ≈ 695k pool)
• #3 Single-request-per-batch: 2 reqs (24,802) > chunked budget (16,384)
• #6 NIXL buffer pool exhaustion: ~6 concurrent 126 MB embeddings
• Agg (RPS=0.71-0.76, 100% success): 2× higher RPS, in-flight 62-83, no NIXL stall
8img/768p — input_len 6,238 (38% of chunked_prefill)
• Disagg (RPS=0.67-0.70, 0%/16% failures):
• #4 max_running_requests=64 cap (in-flight peaks at 63/64)
• #5 Batch degradation: at rate=2.0, single-req batches grow from 26% → 40%
• KV pool only 59% used
• Agg (RPS=0.90-1.49, 100% success): rate=2.0 hits 1.49 RPS (2.2× disagg), latency 16× lower at r=1.0
Improvement Methods
Workload | Method | Estimated Effect
16img/768p | TP=2 aggregate | RPS 0.76 → ~1.4
16img/768p | Reduce per-image vision tokens (smaller patch) | RPS 0.76 → ~1.1 if -25% tokens
8img/768p | --max-running-requests 128 | RPS 0.67 → ~0.78 (KV pool 41% headroom)
8img/768p | Switch to aggregate | RPS 0.67 → 1.49 (2.2× immediate)

## Slide 7
Slide 7 — Case 4 Bottleneck: 4img/768p (input_len = 3,158)
Lightest case. NO bottleneck triggered — system is input-rate-limited. Linear scaling 0.99 → 1.93 RPS.
Workload Profile
• 4 images × 1024×768 → 3,158 input tokens (only 19% of chunked_prefill_size)
• KV demand per req: 3,430; theoretical cap: 202 in-flight
• Embedding size: ~31.5 MB (4× smaller than 8img/1080p)
Disagg Behavior (RPS=0.98-1.79, 100% success)
• NO bottleneck triggered:
• KV pool only 5-9% used (in-flight 11-21 vs 202 theoretical cap)
• max_running_requests=64 not approached (peak 21)
• 5 requests can theoretically merge into one prefill batch (5 × 3,158 < 16,384)
• NIXL buffer pool not exhausted: 768 MB / 31.5 MB = ~24 concurrent (4× headroom vs 8img/1080p)
• System is input-rate-limited (rate=1.0 → 0.98 RPS; rate=2.0 → 1.79 RPS)
Why This Is The Only "OK" Disagg Deployment
• Small per-request workload doesn't stress NIXL ring buffer
• Per-req computation small enough that PD has spare in-flight capacity → buffer drains as fast as it fills
• Estimated true saturation: rate=4.0/np=256 → predicted RPS ~3.0 (linear until max_running=64 caps)
Improvement Methods
Push to rate=4.0 → predicted RPS ~3.0 | --max-running-requests 128 → ~5.0 | TP=2 agg → ~3.5

## Slide 8
Slide 8 — Why Aggregate Wins: Architectural Comparison
Disagg's NIXL handoff is the dominant overhead. Aggregate eliminates it entirely.
Data Flow Comparison
DISAGG E/PD AGGREGATE TP=1 ───────────────── ───────────────── [Encoder process, GPU 0] [Single process, GPU 1] ↓ ViT forward ↓ ViT forward ↓ embeddings (CPU stage) ↓ embeddings (in-memory) ↓ NIXL ring buffer (768MB pool) ←━━┓ ↓ direct tensor handoff ↓ NIXL_WRITE over cuda_ipc ┃ ↓ same CUDA context [PD process, GPU 1] ┃ ↓ LLM prefill+decode ↓ NIXL receive + admit queue ┃ ↓ SGLang scheduler ┗━━ FAILURE POINT under load ↓ LLM prefill+decode (60s timeout, 16-49% reqs lost)
Disagg Overheads Measured
Overhead | Cost | Visible In
NIXL embedding transfer | ~150 ms / req | TTFT gap (1.7s vs 39.9s in 8img/768p)
NIXL ring buffer admission queue | 60s timeout | 4 of 8 benches with failures
PD scheduler admit serialization | ~1.7s per batch tick | running peak = 63 vs agg 67-83
Encoder/PD VRAM split | encoder=0.85 + PD=0.85 | PD KV pool reduced 50%
When Would Disagg Actually Help?
Cross-host: encoder cluster on different machines (RoCE NIXL) | Heterogeneous GPUs: encoder on cheap GPU, decoder on H200 | Shared encoder cache across many decoders | NONE of these conditions apply to single-host single-GPU.

## Slide 9
Slide 9 — Bottleneck Summary Matrix & Improvement Roadmap
Disagg has 0-5 active bottlenecks per case. Aggregate eliminates the NIXL bottleneck (#6) entirely.
Disagg Bottleneck Activation by Case
Bottleneck | 8img/1080p | 16img/768p | 8img/768p | 4img/768p
#1 Chunked-prefill split tail | ✓ (40-46%) | — | — | —
#2 KV pool saturation | ✓ (74%) | ✓ (98%) | — | —
#3 Single-request-per-batch | ✓ | ✓ | — | —
#4 max_running_requests=64 hit | — | — | ✓ | —
#5 Batch degradation under load | — | — | ✓ | —
#6 NIXL buffer pool exhaustion | ✓✓ | ✓✓ | ✓ | —
Active bottlenecks | 5 | 4 | 3 | 0
Disagg RPS / Success | 0.18-0.23 / 50% | 0.33-0.34 / 60% | 0.67-0.70 / 95% | 0.98-1.79 / 100%
Improvement Roadmap (ordered by Effort × Impact)
Priority | Action | Target Case | Estimated Gain
P1 | Switch to TP=1 aggregate for all single-host deployments | All 4 | RPS 2-2.7×, no failures
P2 | Raise --max-running-requests to 128 | 8img/768p, 16img/768p | RPS +10-15%
P3 | TP=2 aggregate (2 GPUs) | 8img/1080p, 16img/768p | RPS ~2× more
P4 | --chunked-prefill-size 32768 | 8img/1080p | RPS +30-40% (test for OOM)
P5 | Lower image resolution / fewer images | 8img/1080p → 8img/768p | RPS 2× (0.47 → 0.90)
P6 | Patch SGLang for chunked-prefill tail-coalescing | 8img/1080p | RPS +20% (multi-day work)

## Slide 10
Slide 10 — Recommendations & Next Steps
Universal recommendation: TP=1 aggregate for single-host. Disagg only valuable cross-host.
Production Deployment Recommendations
Workload | Recommended | Backup | Avoid
8img/1080p | TP=1 agg (0.47 RPS) or TP=2 agg (~0.95) | Resolution reduction | Same-host disagg (50% fail)
16img/768p | TP=1 agg (0.71 RPS) or TP=2 agg | Image count reduction | Same-host disagg (40% fail)
8img/768p | TP=1 agg (0.90-1.49 RPS) | TP=2 agg | Same-host disagg at rate≥1.5
4img/768p | TP=1 agg (0.99-1.93 RPS) | Same-host disagg (acceptable) | —
Frontend Admission Control (required for any disagg deployment)
• Monitor PD running-req, return HTTP 429 when ≥ 60
• Monitor NIXL ring buffer occupancy, throttle when > 80%
• Stagger receive_timeout vs encode_timeout (currently both 60s — avalanche risk)
Validated Performance Models
• RPS = total_token_throughput / (input_len + output_len) — verified within 1.2% across 16 datapoints
• Aggregate ceiling: GPU compute throughput (~9,500 tok/s sustained on H200 FP8)
• Disagg ceiling: NIXL_MAX_BUFFER_SIZE / per_req_embedding_size × PD_admit_rate
Next Experiments
TP=2 aggregate full sweep at np=128 to quantify additional speedup | --chunked-prefill-size 32768 on 8img/1080p | --max-running-requests 128 sweep | Cross-host disagg with B70 encoder + H200 PD